## Slide 1: Programmering og Problemløsning
3.2+3: Verbose og letvægtssyntaks, funktioner, virkefelter, dokumentation, betingelser, mutérbare værdier (variable), løkker, tupler

## Slide 2: Virkefelter (scope)
let name = "World"
let name = "Jon"
do printfn "Hello %s" name
Navne (i yderste virkefelt) kan ikke overskrives
let greeting = "Hello"
let name = "Jon"
do printfn "%s %s" greeting name
(
let name = "Anders"
do printfn "%s %s" greeting name
)
do printfn "%s %s" greeting name
Virkefelter via parenteser
0
1
name = "Jon" greeting = "Hello"
name = "Anders"
...
...
0
1
2
...

## Slide 3: Syntaks og virkefelter
let name = "World"
do printfn "Hello %A" name
let name = "World" in do printfn "Hello %A" name
Letvægtssyntaks
verbose syntaks
let name = "World"
printfn "Hello %A" name
Valgfrit ’do’

## Slide 4: Funktioner
let greetings (name : string) : string =
"Hello " + name
Organisering = nemmere at forstå og vedligeholde
let greetings name =
"Hello " + name
let greetings name = "Hello " + name
let greetings name : string = "Hello " + name
let greetings (name : string) = "Hello " + name
Leksikografisk virkefelt
Indryk angiver funktionskroppen
let str = greetings "Jon"
printfn "%s" str
printfn "%s" (greetings "World")
> let greetings (name : string) : string =
- "Hello " + name;;
val greetings : name:string -> string

## Slide 5: Løs en andengradsligning (baglæns!)
let solution a b c sgn = -3.4
let discriminant a b c =
b ** 2.0 - 4.0 * a * c
let a = 1.0
let b = 0.0
let c = -1.0
let xp = (solution a b c +1.0)
printfn "0 = %fx^2 + %fx + %f => x_+ = %f" a b c xp
Mockup funktion
let solution a b c sgn =
let d = discriminant a b c
(-b + sgn * sqrt d) / (2.0 * a)

## Slide 6: Dokumentation - simpel
/// The discriminant of a quadratic equation with parameters a, b, and c
let discriminant a b c = b ** 2.0 - 4.0 * a * c // Note that F# will automatically typecast to float
(* This function needs to be tested! *)
Summary felt efter dokumentationsstandarden
Almindelig kommentarer udenfor dokumentationsstandarden

## Slide 7: Dokumentation - grundig
/// <summary>Find x when 0 = ax^2+bx+c.</summary>
/// <remarks>Negative discriminants are not checked.</remarks>
/// <example>
/// The following code:
/// <code>
/// let a = 1.0
/// let b = 0.0
/// let c = -1.0
/// let xp = (solution a b c +1.0)
/// printfn "0 = %.1fx^2 + %.1fx + %.1f => x_+ = %.1f" a b c xp
/// </code>
/// prints <c>0 = 1.0x^2 + 0.0x + -1.0 => x_+ = 0.7</c> to the console.
/// </example>
/// <param name="a">Quadratic coefficient.</param>
/// <param name="b">Linear coefficient.</param>
/// <param name="c">Constant coefficient.</param>
/// <param name="sgn">+1 or -1 determines the solution.</param>
/// <returns>The solution to x.</returns>
let solution a b c sgn =
let d = discriminant a b c
(-b + sgn * sqrt d) / (2.0 * a)

## Slide 8: XML dokumentationspipeline
commentExample.fsx
commentExample.xml
commentExampleHTML
index.html
fsharp --doc
mdoc update
mdoc export-html
fsharpc --doc:commentExample.xml commentExample.fsx
mdoc update -o commentExample -i commentExample.xml commentExample.exe
mdoc export-html -out commentExampleHTML commentExample

## Slide 9: Betingelser
> let str =
- if 3 < 2 then
- "3 < 2"
- elif 3 = 2 then
- "3 = 2"
- else
- "3 > 2";;
val str : string = "3 > 2"
Kæde af betingelser
> if 3 < 2 then
- printfn "3 < 2"
- else
- printfn "3 >= 2";;
3 >= 2
val it : unit = ()
If-then-else
> let str =
- if 3 < 2 then
- "3 < 2"
- else
- "3 >= 2";;
val str : string = "3 >= 2"

## Slide 10: Muterbare værdier og løkker
let mutable i = 1
while i <= 10 do
printf "%d " i
i <- i + 1
printf "\n"
let mutable x = 5
printfn "%d" x
x <- -3
printfn "%d" x
for i = 1 to 10 do
printf "%d " i
printfn ""

## Slide 11: Hvad gør programmet?
let i = 0
while i < 3 do
let i = i + 1
printfn "%d" i
i på højre side er altid 0

## Slide 12: Tupler
> printfn "%A %A" (fst a) (snd a);;
1 1.0
val it : unit = ()
> let (b1, b2, b3) = b;;
val b3 : char = '1'
val b2 : string = "en"
val b1 : int = 1
$fsharpi
…
> let a = (1, 1.0);;
val a : int * float = (1, 1.0)
> let b = 1, "en", '\049'
val b : int * string * char = (1, "en", '1’)
> let mutable c = (1,2)
- c <- (2,3)
- printfn "%A" c;;
(2, 3)
val mutable c : int * int = (2, 3)
val it : unit = ()
Produkttype
Parentes unødvendig men anbefalelses
Funktioner til at indicerer i par
Venstre side af en binding kan have navngivne tuple-elementer
Hele typen - ikke enkelt - elementer kan være mutérbare

## Slide 13: Fibonacci
let mutable m = 1
let mutable n = 1
let N = 5
for i = 3 to N do
let p = m + n
m <- n
n <- p
printfn "%d: %d" N n
let mutable m = 1
let mutable n = 1
let mutable i = 3
let N = 5
while i <= 5 do
let p = m + n
m <- n
n <- p
i <- i + 1;
printfn "%d: %d" N n
let mutable pair = (1,1)
let N = 5
for i = 3 to N do
pair <- (snd pair, fst pair + snd pair)
printfn "%d: %d" N (snd pair)
For-løkke
While-løkke
Tupple + for-løkke
let fib N =
let mutable pair = (1,1)
for i = 3 to N do
pair <- (snd pair, fst pair + snd pair)
snd pair
let N = 5
printfn "%d: %d" N (fib N)

## Slide 14: Decimal til Binær
let N = 116
let mutable n = N
let mutable str = ""
while n > 0 do
let rest = n % 2
n <- n / 2
if rest > 0 then
str <- "1"+str
else
str <- "0"+str
printfn "%d_10 = %s_2" N str
let N = 116
let mutable n = N
let mutable str = ""
while n > 0 do
str <- (if n % 2 > 0 then "1" else "0") + str
n <- n / 2
printfn "%d_10 = %s_2" N str